## Slide 1: Hackathon risc-v & ai Ofek ben atar amit zohar

## Slide 2: Hackathon mission
  AI Accelerator that performs matrix convolution for image processing
  Kernel matrix : 3X3
  Data matrix : 4X4
  Memory management using C language

## Slide 3: MEMORY MANAGMENT
  Memory Structure : 7 registers
  Kernel Registers : m1-m3
  Data Registers : d1 – d4
Kernel
Data

## Slide 4: Solution
For maximum efficiency we created a module named “multiplier9by9” which performs the vector dot product parallelly
This module calculates one iteration of the convolution
Maximum use of hardware for minimum time

## Slide 5: Average & variance calculation
    AVERAGE
    Module that receives the convolution matrix and returns it’s average
    Firstly, we have added all the matrix cells into 16’ bits wire
    In order to divide the sum by 4 we used shift right by 2
    We used this module in order to normalize the data
    VARIANCE
    Module that receives the convolution matrix and returns its variance
    Representing the result as 16’ bits, implementing cutoff method

## Slide 6: Our additional features
OUTPUT | SW[8] | SW[9]
Convolution | 0 | 0
Normalized Convolution | 1 | 0
Average | 0 | 1
Variance | 1 | 1
BLUR | S7[7]
Gaussian | 0
Box | 1
In order to show all the data we added switch functionality to control the 7Segment output
We added extra kernel of type “Box Blur” in addition to the default “Gaussian Blur” Kernel (That we set with C program)
Box Blur
Gaussian Blur